## Slide 1: WiFi Authentication [Beacon Manipulation]
2023.06.19.
GyeongHeon Jeong(ghjeong@mmlab.snu.ac.kr),
SangWi Kang(swkang@mmlab.snu.ac.kr)

## Slide 2: WiFi authentication
AP
Mobile
Terminal
Validate signature
Server
Cert.
Continue connection
Raspi
Signature
Generate key-pair
&
Get Cert.
Beacon Frame

## Slide 3: Contents to do
AP make private key and public key pair, and get certificate
2 ways to give cert+signature
  1. Cert+signature in beacon frame
  2. Give user cert+signature packet after connection request
User validate signature with AP’s public key
  User can figure out REAL AP
AP
Mobile
Terminal
Raspi
Origin beacon frame
Cert.
Signature

## Slide 4: Project Progress
AP의 key-pair 및 인증서 생성
  RSA 512, 1024, 2048
  ECDSA 256, 384, 521
AP 동작 핵심 프로그램인 hostapd 분석 (Raspberry Pi OS)
  Beacon interval, SSID 등 primitive type 위주 수정
Hostapd beacon logic 분석 지연으로 구현 방향 변경
  Beacon manipulation with Python Scapy
  Signature parsing by client kernel modification

## Slide 5: Beacon Manipulation

## Slide 6: Signature Parsing
Packet arrival
ieee80211_rx_handlers()
ieee80211_scan_rx()
ieee80211_rx_h_mgmt_check
Beacon frame access method
ieee80211_bss_info_update()
ieee80211_update_bss_from_elems()

## Slide 7: Signature Verification
Cert. verification
Get Public key in cert.
&
Signature Verification

## Slide 8: Experiment & Result (Frame Size)
Chart: 
| RSA 512 | RSA 1024 | RSA 2048 | ECDSA 256 | ECDSA 384 | ECDSA 521 | Plain
열1 | 810 | 1052 | 1534 | 812 | 931 | 1062 | 84
(bytes)

## Slide 9: Experiment & Result (Delay)
Chart: 
| RSA 512 | RSA 1024 | ECDSA 256 | ECDSA 384 | ECDSA 521 | Plain
열1 | 165.3509 | 163.135 | 166.2574 | 167.3732 | 165.2405 | 156.7532
(ms)
  Beacon tx delay – From signature generation to beacon sending

## Slide 10: Thank you for listening